## Slide 1
Gaurav Mahamuni1, Mingyu Wang1 and Su Ye2
1Mechanical Engineering, University of Washington, 2Computer Science and Engineering, University of Washington
CSE 547: Machine Learning for Big Data
SEMI-SUPERVISED LOGISTIC REGRESSION RESULTS
Air Pollution Mapping and Prediction
BELLKOR RECOMMENDATION RESULTS
MODELS / ALGORITHMS
ABSTRACT
DATA
CONCLUSIONS
FUTURE WORK
ACKNOWLEDGMENTS
Particulate Matter (PM) analysis is important in assessing an individual’s exposure to potentially harmful particles.
Currently, PM is recorded at sparse locations in a geographical area, however, the PM level can vary dramatically over small distances.
We map and predict PM levels at specific locations in the city of Krakow in Poland from spatio-temporal data of PM levels and meteorological data.
Measurement of the PM level trend using Bellkor recommendation system achieved overall R2 =0.928.
We classify PM concentrations into 6 classes using semi supervised L1-regularized logistic regression. The model has 69.4% mapping accuracy and 61.5 % - 51.7 % prediction accuracy for 1 - 4 hrs.
Generating an algorithm that can accurately calculate the derivative of the interpolated data for data driven discovery of PDE.
Improving feature selection using different algorithms in semi-supervised classification.
This project was a part of CSE547 Machine Learning for Big Data Course. We thank Prof. Tim Althoff for his feedback.
Figure 2. Overall distribution of sensors and average normalized pollution at sensor locations for 10 months in 2017
Gaurav Mahamuni gauravsm@uw.edu Mingyu Wang myw518@uw.edu Su Ye yes23@uw.edu
We have two kinds of data in the dataset for each sensor: 1) Meteorological data: temperature, humidity and barometric pressure.
2) Air quality data: PM2.5, PM10 and PM1.
Figure 1. In the year 2016, ambient air pollution was responsible for 4.2 million deaths
Figure 7. PM2.5 concentration labels for 7th March 6:00 AM at all 29 sensor locations (left) and PM2.5 concentrations mapped by semi-supervised L1-regularized logistic regression model.
Semi-supervised Classification using L1-regularized Logistic Regression
DATA DRIVEN DISCOVERY OF PDE
Data-Driven Discovery of Partial Differential Equations (PDE)
Figure 3. The relative position for test data with respective to all other training sensors
This model can measure the overall trend with R2=0.928.
The model does not perform well for current time trend (best R2 = 0.484).
The model is not suitable for prediction due to low accuracy which might be due to missing features in data.
Bellkor recommendation system
Prediction Based on Radial Basis Function Interpolation
Training data Matrix
Figure 4. Pollution data over 10 months for 6 sensors. The pollution levels are higher in the fall and winter months.
Partial Differential Equation Generated By Algorithm 3
Figure 5. Comparison of latent factor model results (red) vs true records (blue) .
Figure 6. Accuracy considering year vs month data.
Notes: 1